## Slide 1: Semantic Interoperability
T2TRG/WISHI

## Slide 2: Outline
Semantic Interoperability
Example: IPSO Temperature Object
OCF mapping
  Direct use of of IPSO Identifiers
  Mapping to OCF Identifiers
  RAML and JSON Schema
Layered Semantic Interoperability
  Protocol-neutral semantic vocabulary - iotschema
  Hypermedia controls – W3C Thing Description

## Slide 3: Semantic Interoperability
Practical definition: Resolve "What to do" and "How to do it"
"What to do" is a problem of horizontal normalization – of semantic concepts and meta models
"How to do it" is a problem of vertical integration – of diverse data models and protocols
Workflow tends to break down into discovery and configuration phase (What to do) and operation phase (How to do it)

## Slide 4: IPSO Smart Objects
Meta-model, based on OMA LWM2M, consisting of reusable definitions for:
  Objects, which encapsulate some modular function like a measurement
  Resources, which each represent a simple value that exposes or describes the function of the Object
  An Object is a collection of Resources
Semantic interoperability is achieved through a pre-defined set of Object and Resource identifiers
LWM2M Protocol "baggage" and constraints

## Slide 5: Example: IPSO Temperature Object Definition – also XML file
Object | Object ID | Object URN | Multiple Instances? | Description
IPSO Temperature | 3303 | urn:oma:lwm2m:ext:3303 | Yes | Temperature sensor, example units = Cel
Resource Name | Resource ID | Access Type | Multiple Instances? | Mandatory | Type | Range or Enumeration | Units | Description
Sensor Value | 5700 | R | No | Mandatory | Float |  |  | 
Units | 5701 | R | No | Optional | String |  |  | 
Min Measured Value | 5601 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | 
Max Measured Value | 5602 | R | No | Optional | Float | Same as Measured Value | Same as Measured Value | 

## Slide 6: IPSO Temperature Object Representation
GET /3303/0
[
{"bn": "3303/0/" },
{"n": "5700", "v": 27},
{"n": "5701", "v": "Cel" },
{"n": "5601", "v": 22 },
{"n": "5602", "v": 40,
{"n": "5603", "v": 0 },
{"n": "5604", "v": 100 }
]

## Slide 7: OCF
OCF uses a meta model consisting of Resources that expose multiple Properties
The format is a JSON-like object with named properties
RAML and JSON Schema are used to specify the properties of a typed resource and the possible interactions as CRUD operations
OCF uses RFC 6690 style links to index resources and create collections of resources
OCF allows links and batch interactions on a collection resource

## Slide 8: OCF Example – Temperature Resource using IPSO identifiers
GET /3303/0
{
"5700": 27,
"5701": "Cel",
"5601": 22,
"5602": 40,
"5603": 0 ,
"5604": 100
}

## Slide 9: OCF Example – Temperature resource Re-using OCF Identifiers
GET /example/temperature?if=oicif.s
{
"temperature": 27,
"units": "Cel",
"range": [0, 100],
"minimum": 22,
"maximum": 40,
"resetminmax": false
}
GET /oic/res?if=oicif.ll
{
"href": "/example/temperature",
"if": ["oic.if.baseline","oic.if.s"],
"rt": ["oic.r.temperature", "oic.r.minmax"]
}

## Slide 10: Semantic Interoperability using IPSO and OCF
Semantic model, data formats, and protocols are tightly coupled
"What to do" and "How to do it" are defined in schemas and by type tags
Modular and composable, but only intra-operable with compatible devices

## Slide 11: De-coupled approach
"What to do" and "How to do it" can be decoupled
"What to do" can be defined in a protocol-neutral and format-neutral way
  Like ontologies and vocabularies
"How to do it" can be defined in a way that takes advantage of network interoperability and accommodates diverse formats and interaction models
  Like hypermedia controls

## Slide 12: Layered Scope in Data Models and Information Models
Data Models
Information Models
OCF
LWM2M
W3C WoT Thing Description (Application Facing Media Type)
iot.schema.org Capabilities (Event, Action, Property)
Device Specific Protocols: OCF, LWM2M, IPSO, dotdot
Semantic annotation
Protocol Binding
(…)
"What I want to do"
"How to do it"

## Slide 13: iotschema
Patterned after schema.org
RDF definitions for connected things
Start with common definitions for the common affordances of things
Apply a simple meta model that captures existing models and functionality
Create a venue where specific definitions may be developed for vertical market applications

## Slide 14: iotschema Capability Pattern
schema:thing
Capability
InteractionPattern
Action
Event
Property
schema:PropertyValue
schema:PropertyValueSpec.
acceptsInputData
providesOutputData
providesInteractionPattern
schema:EntryPoint
schema:target
rdfs:subclassOf
schema:Property
iotschema Class
Reused Class

## Slide 15: Examples of Capabilities
Thing | Capabilities | Properties | Type | Actions
Motion Sensor | Motion Sensing | Motion | Boolean | (read)
Temperature | Temperature Sensing | Temperature | Number | (read)
Light | Switch | SwitchState | Boolean | TurnOn TurnOff
Light | Level Control | Level TransitionTime | Number Number | MoveToLevel MoveLevel StepLevel

## Slide 16: Example iotschema Definition
"type": "LevelCapability",
"id": "iotschema:LevelCapability",
"subClassOf": "Capability",
"description": "Level Sensing and Control Capability",
"providesInteractionPattern": {
"level": {
"type": "Property",
"name" : "level",
"acceptsInputData": {
"type": "schema:Number",
"schema:valueName": "level",
"schema:unitCode": "ucum:%"
},
"providesOutputData": {
"type": "schema:Number",
"schema:valueName": "level",
"schema:unitCode": "ucum:%"
}
},

## Slide 17: Example Definition (cont'd)
"moveToLevel": {
"type": "Action",
"name": "moveToLevel",
"acceptsInputData": {
"level": {
"type": "schema:Number",
"schema:valueName": "level",
"schema:unitCode": "ucum:%"
},
"transitionTime": {
"type": "schema:Number",
"schema:valueName": "transitionTime,
"schema:unitCode": "ucum:s"
}
}
}

## Slide 18: W3C WoT Thing Description
Patterned after hypermedia controls
Describes "What to do" in a common meta model format, without any application specific vocabulary
  Semantic annotation from third party sources like iotschema
Describes "How to do it" using a protocol binding technique
  Hyperlinks, Payload templates, and transfer layer descriptions

## Slide 19: Example Instance – TD Interaction
{
"@type": ["action", "sch:movetolevel"];
"name": "set brightness level",
"inputdata": {
"type": "object"
"field": {
"level": {
"type": "number",
"@type": "sch:level"
},
"time": {
"type": "number",
"@type": "sch:transitiontime"
}
}
},

## Slide 20: Example Instance – TD Protocol
link: [
{
"href": "coap:10.0.0.17:8000/light/brightness",
"mediatype": "application/vnd.ocf+cbor",
"method": "ocf.update",
"rt": ["oic.r.brightness", "oic.r.ramptime"],
"if": ["oic.if.a", "oic.if.baseline"],
}
}
]