## Slide 1: WoT Thing Description Protocol Binding Template for OCF
Michael J Koster
June 8, 2017

## Slide 2: Protocol Binding
Maps abstract operations on WoT meta types to concrete operations on target resources
WoT
  Properties (get, set)
  Actions (invoke, cancel)
  Events (subscribe, unsubscribe)
OCF
  CRUD+N Resource Model, resource types, interface types, collections, actuation

## Slide 3: Protocol Binding Template
A specification for the information included in a particular protocol binding, and its format
TD Interaction Description contains information common to all protocol bindings
Protocol Binding contains information needed to make requests and process responses
Protocol Binding Template indicates which information is included for a particular protocol

## Slide 4: Thing Description (simplified)
{
"@type": ["thing", "sch:light"],
"name": "Example Light Thing",
"interactions": [
{
"@type": ["action", "sch:setlevel"];
"name": "set brightness level",
"inputdata": {
"type": "number"
"@type": "sch:level.value"
},
"links": [
{ "href": "/example/light" },
{...}
]
},
]
}
Interaction Description
Protocol Binding

## Slide 5: OCF Protocol Binding Structure
Basic form of a hypermedia control, extension to the "links" property
  link attributes describe high level operations
  method, interface type, resource type, schema mapping to input/output data in TD
Properties included in the OCF Protocol Binding
  method (ocf.retrieve, ocf.update…)
  rt - resource type
  if - interface type
  mediatype (default "application/vnd.ocf+cbor")
  schemas for inputdata/outputdata element

## Slide 6: TD – Interaction Description
{
"@type": ["action", "sch:setlevel"];
"name": "set brightness level",
"inputdata": {
"type": "object"
"properties": {
"P0001": {
"type": "number",
"@type": "sch:level.value"
},
"P0002": {
"type": "number",
"@type": "sch:transitiontime.value"
}
}
},
"links": [
(protocol binding goes here)
]
}
JSON Schema
+ Extension

## Slide 7: TD - Protocol Binding
links: [
{
"href": "coaps://[fdfd::22]/example/light/bright",
"content-format": 1000,
"method.invoke": "post",
"rt": ["oic.r.brightness", "oic.r.ramptime"],
"if": ["oic.if.a"],
"inputschema": {
"type": "object",
"properties": {
"brightness": {
"value": "{{P0001}}"
},
"ramptime": {
"value": "{{P0002}}"
}
}
}
}
]
JSON Schema
+ Extension

## Slide 8: Integration Patterns
ConsumedThing API
WoT Application
node-wot
(ExposedThing API)
WoT Application
ConsumedThing API
WoT Network
OCF Network
OCF Network
Client
Client
Client
Server
Client
iotivity
iotivity-node
resource server
Client Proxy
Server
Server Proxy
OCF ProtocolClient
protocol binding
protocol binding
node-wot
iotivity-node
iotivity
iotivity-node
iotivity

## Slide 9: Protocol Binding Processing for Client Proxy Pattern
WoT Application
Protocol Binding Runtime + iotovity
TD
OCF Network
PB
Template Engine
WoT Runtime
ProtocolClient
ConsumedThing API
Instances

## Slide 10: Protocol Binding Processing for Server Proxy Pattern
WoT Runtime
Protocol Binding Runtime + iotovity
TD
OCF Network
PB
Template Engine
Server Proxy
ExposedThing API
Instances
WoT Network
Simple TD

## Slide 11: Discovery
Applications discover things using TD templates containing semantic constraints
TD instances could be pre-generated for all OCF discovered devices, and registered with a TD discovery service
New devices could be registered upon OCF discovery
Alternatively, OCF discovery queries could be mapped from Thing Descriptions and submitted on demand

## Slide 12: Mapping OCF to WoT
OCF Device maps to Wot Thing
An OCF device contains a set of resource type instances
An OCF resource type instance contains a set of properties
Multiple properties may be retrieved or updated in a single interaction, e.g. a value and a time stamp
OCF properties map to TD properties
Some OCF properties map to TD property value attributes (min, max, step, units)

## Slide 13: Mapping OCF to TD Actions
With OCF, Actions are invoked using updates to properties
Multiple properties may be updated in a request, for example light brightness and ramp time, by sending a structure
OCF does not define actions per se

## Slide 14: Capability-based mapping
Capabilities are Action, Event, and Property definitions for a single function
On/off control is a capability with an on/off boolean state property, and either an on action and an off action, or a state change action that has a boolean input parameter
Level control is a capability with level and transition time properties, and a setlevel action with level and transitiontime input parameters

## Slide 15: Capability-based mapping
An OCF light exposes a binary switch resource, a brightness control resource, and a ramp time resource
OnOff and level capabilities can be used to map the binary switch and brightness + ramptime resources, respectively
TD exposes the properties and actions for onoff and level, and maps them to the OCF resources and methods

## Slide 16: Examples
Examples in this presentation may be found in:
https://github.com/mjkoster/wot-protocol-binding