## Slide 1: Conditional Notification
Some Examples
Michael Koster
13 December 2017

## Slide 2: Conditional Notification
Controls for Asynchronous Notification
Results in a sequence of notifications that conforms to a filter specification
Consist of time and value threshold controls
Examples from IETF CoRE, OMA LWM2M, and OCF

## Slide 3: IETF – CoRE Dynlink (draft)
Split from the CoRE Interfaces Draft
OMA LWM2M follows the vocabulary
Time threshold controls are "pmin" and "pmax"
Value threshold controls "gt", "lt", and "st" apply to scalar values only; e.g. numbers
Band mode for notification control based on value range

## Slide 4: Threshold controls
pmin is the minimum time interval between notifications, even if data are changing more frequently
pmax is the maximum time interval between notifications, even if data have not changed
st (step) is the minimum reportable change in data value, relative to the most recent notification
lt (less than) is the low value reporting threshold
gt (greater than) is the high value reporting threshold

## Slide 5: Reporting mode
Simple threshold mode (default)
  report whenever lt or gt thresholds are crossed in either direction
Band mode (when the "band" parameter is included or set to true)
  report when the sample is between lt and gt values, according to pmin, pmax, and st
  gt may be less than lt, resulting in reporting only outside the band
  some systems may allow more than one band to be active at a time

## Slide 6: Conditional Observe
Conditional Notification controls may be configured in URI parameters of Observe operations
GET coap://[fdfd::13]/remote?pmin=1&pmax=300&st=1
Minimum reporting period
Maximum reporting period
Reportable value change (step)

## Slide 7: CoRE Dynlink Bindings
Dynamic Link Bindings are hyperlinks which configure dynamic data transfers
Links with the "boundto" link relation point to the source of notification data
Notification data are transferred to the link context
Notification parameters are encoded as link target attributes
Link Bindings are created and stored in one or more binding tables (collections) at the server with rt=core.bnd

## Slide 8: CoRE Dynlink example (local update)
{
"anchor": "/local/resource",
"rel": "boundto",
"href": "coap://[fdfd::13]/remote",
"pmin": 1,
"pmax": 300,
"st": 1
}
Minimum reporting period
Maximum reporting period
Reportable value change
Resource to be updated
Resource to be observed

## Slide 9: CoRE Dynlink example (remote update)
{
"anchor": "coap://[fdfd::13]/remote",
"rel": "boundto",
"href":"/local/resource",
"pmin": 1,
"pmax": 300,
"st": 1
}
Minimum reporting period
Maximum reporting period
Reportable value change
Resource to be updated
Resource to be observed

## Slide 10: OMA LWM2M Notification Control
OMA LWM2M Notifications are sent from the LWM2M Device to some application handler in response to CoAP Observe
LWM2MConditional Notification parameters are configured on an object or resource using the "Write Parameters" operation:
PUT coap://[fdfd::13]/3303/0?pmin=1&pmax=300&st=1
(empty payload)

## Slide 11: OCF Conditional Notification
OCF Conditional Notification is a resource type that is composed with another resource in order to control notification (one setting per resource instance)
Properties are minnotificationperiod, maxnotificationperiod, and threshold
The definitions correspond to pmin, pmax, and step, respectively
Threshold uses the same units and scale as the measurement data

## Slide 12: OCF Conditional Notification
POST /example?rt=oic.if.notification.conditional
(payload)
{
"minnotificationperiod": 1,
"maxnotificationperiod": 300,
"threshold": 1
}
Minimum reporting period
Maximum reporting period
Reportable value change

## Slide 13: Notification Patterns
Observe with a sequence of responses, e.g. CoAP, eventsource, websockets
Publish/Subscribe using a broker, e.g. MQTT
Web Hook, e.g. HTTP PUT/POST to URI, external update link binding
Notification queue
With or without created subscription resources

## Slide 14: Subscription creation
Sometimes a resource already exists from which notifications can be obtained using observe (or retrieve)
Sometimes a resource is created, from which notifications are them obtained through some address or handle – this resource may be deleted when the workflow terminates
The websocket notification design uses this pattern in order to share a websocket connection over different notifications

## Slide 15: Subscription Creation
With Pub/Sub, a new topic may be created on which to receive the notifications
A Dynamic Link or Web Hook is a sort of created subscription that pushes updates to another server
A "monitor" resource may be created and updated using a dynamic link, from which to obtain notifications using Observe
Such a monitor resource may also store notifications to be retrieved in bulk

## Slide 16: What is an Event?
An event is a state change that conveys more than a simple property state change
Separate the semantics of an event from the mechanism for receiving Event notifications
For example, a button may emit shortpress, logpress, and doublepress events that are related to change patterns in the button state over time
Events and Property change notifications can use the same mechanisms – observe, pubsub, web hooks, with and without created subscriptions